| Pressure Equipment Manufacturer: |
| --- |
| PMA Ref. No. | Rev. | Material Group for Welding |
| Material specification including date: | Grade: | Delivery condition: |
| Product Form: | Application: |
| Applicable Design Code: | Dimension range: |
| Maximum allowable temperature: | Minimum allowable temperature: |
| Compliance with Essential Safety Requirements for materials |
| Property | Requirement | Details of Compliance * (to be verified on material certification) |
| Appropriate properties (Annex I - 4.1(a)) (Assured by material manufacturer) | Proof strength/Yield strength (at appropriate temperature) UTS Creep data | Quote R e; R e/, R m, R m/t/T etc from material specification or where appropriate properties are obtained |
| Sufficiently ductile (Annex I - 4.1(a)) (Annex I – 7.5) | In steel; A min 14% | Quote minimum elongation specified in material specification, A min long % A min trans % |
| Sufficiently tough (Annex I - 4.1(a)) (Annex I – 7.5) | e.g. in steel; KV min 27J at 20 ºC or lowest operating temperature. | Quote impact strength and coincident minimum temperature specified in material specification or provide justification per WGP Guideline 7/17 |
| Not significantly affected by ageing (Annex I – 4.1(c)) | No specific quantitative requirement specified | a) Select materials that are not liable to (strain) ageing b) confirm that material specification ensures Al:N2 ratio > 2:1 c) confirm plastic deformation not sufficient to cause strain ageing. |
| Suitability for intended processing (Annex I - 4.1(d)) | No specific quantitative requirement specified | Manufacturer must select materials that have appropriate properties for the intended manufacturing processes, e.g. for welding (carbon equivalent), forming (ductility), heat treatment (composition, section size, etc). |
| Material Certification | Cat I - Certificate affirming compliance with the specification. Cat II, III & IV - Certificate of Specific Product Control. | Certification according to EN 10204:2004 Test Report "type 2.2" Certification according to EN 10204:2004 Inspection Certificate "type 3.1" or "type 3.2" |
| Material Marking | Traceability to heat/lot identity of the material manufacturer | Method of traceability to the certification supplied by the material manufacturer. |

* Contents of this column are provided for guidance to the responses required, other solutions may be equally valid.

Additional Requirements:

1

The named material may be used for the construction of pressure equipment intended for use within the stated limits and subject to the following restrictions:

- *e.g. Restrictions: Carbon 0.22% max, Sulphur 0.015% max, Phosphorus 0.020% max

Signed:								Date:

(Pressure Equipment Manufacturer)

Confirmed:								Date:

(Notified Body (Category III & IV only))